Tim Herbert & Sandra Burrill

51 Peterson Road

675-2036

Permit # 2016-52

Map/Lot 107/35

1-1/2 story addition porch with second floor

1089 Route 12A

06-21-16	Permit - applying, 1089 Route 12A. Met with Tim and his wife to discuss plans to add an addition to the rear of the house that will be an enclosed porch with or without a second floor. They finally decided to have the second floor above the porch. The upstairs bedroom goes from the front to the back of the house and the rear window will not go outside for egress and the front window is too small and will have to be changed. Tim will draw up plans to submit with permit application.

Time 1.0

07-19-16	Permit - applying, 1089 Route 12A. Inspected the wall framing and the ceiling framing for the addition. June report has information about my meeting with him prior to permit application.

Time 0.3

04-20-17	Permit 2016-52, 1089 Route 12A. Met Jim O to inspect rough in electrical 		wiring of enclosed porch (first stage of 1-1/2 story addition on rear of 			house), everything was okay.

Time 0.3

06-27-17	Permit 2016-52, 1089 Route 12A. I inspected the walls and rafters for the 			second floor. Framing looked okay.

Time 0.4

10-06-17	Permit 2016-52, 1089 Route 12A. Only a few siding boards on the north side between the two roofs. Everything else is completed on the first floor. The second floor will be done at a later date under a new permit.

I want to see the upstairs before I issue a CO for the addition which includes the replacement of the bedroom window, 12A end, with an egress window for upstairs bedroom in the house. Already installed.

Time 0.4

10-16-17	Permit 2016-52, 1089 Route 12A. All the siding completed. I will issue a Completion Certificate for the screened porch and when the upstairs is completed on a new permit and work is completed a CO can be issued.

David H Lersch

Plainfield Building Inspector