Peter Whybrow

10724 Wilshire Blvd. APT 1104

Los Angeles, Ca 90024

310-206-1233

Permit # 2013-16

Map/ID #  225/3

Replace 8x24 porch, add 24’ dormer

119 Westgate Road

07-18-13	Permit 2013-16, 119 Westgate Road. Emily Electric called to have the rough in electrical inspection done. Rough in was okay. I also inspected the framing of the dormer and the additional supports for the roof. I also inspected the porch that was almost finished. Look okay.

Time 0.8

10-22-13	Permit 2013-16, 119 Westgate Road. I went to do the final inspection of the dormer that contains the finished two bedrooms, the rest of the second floor is still unfinished. The porch is competed and is okay. There is a lot of fixing up being done and I said that he should have a permit as some walls will be removed to make the kitchen larger and have a large opening to the front room that will be the dining room. Windows were replaced in the bedrooms and were they were inserts (do not meet egress requirements) and not required to meet code per town of Plainfield. Smoke detectors were not installed and electrician will be installing one in each bedroom, one at top of stairs, one in basement, and one in the room that will be the dining room as it will be open to the stairs and most of the first floor. Johanna will call when they are installed and I can issue a Certificate of Completion for the work that was completed under the permit.

Time 0.5

David H Lersch

Plainfield Building Inspector