Richard Jr & Barbara Parker

109 Route 4A Lebanon

252-9964

Permit # 2014-89

Map/ID # 105/19

SFH on unfinished basement at

12 Baynes Road

12-08-04	Perimeter drains inspected when construction was Meriden Village 			Development and foundation was covered until now.

12-30-14	Permit 2014-89, 12 Baynes Road. Win inspected the new electrical service and gave the okay to energize.

Time 0.5

03-27-15	Permit 2014-89, 12 Baynes Road. I inspected the framing. They had replaced all the joists and plates that were constructed in 2004 and covered. They installed three inches of blue foam on the crushed stone and installed radiant heat pipes and poured the floor. Radon pipes were already installed in the stone and now extend above the floor and will go up through to the roof.

Time 0.8

05-11-15	Permit 2014-89, 12 Baynes Road. I inspected the rough in electrical and 			plumbing. All the drain pipes were caped and pressure tested as well as the 		water pipes. They will call for the insulation inspection. They are building 			for the energy star rating.

Time 0.9

05-14-15	Permit 2014-89, 12 Baynes Road. I inspected the footer forms for the 			attached garage and all was okay.

Time 0.4

05-15-15	Permit 2014-89, 12 Baynes Road. I did the insulation inspections. It was blown in. I also checked the holes that needed the fire stop. The insulation installers did the fire stopping also. Looked okay. I also inspected the frost wall forms for the attached garage.

Time 0.6

07-02-15	Permit 2014-89, 12 Baynes Road. I inspected some additional rough in plumbing and electrical in the garage. Looked okay, more to be completed and pressure tested. Also holes need to be fire stopped.

Time 0.4

07-06-15	Permit 2014-89, 12 Baynes Road. I went by to see the progress and when to do the final rough in and insulation inspection. Inspected what was completed so far and the rough in should be completed today and pressure tested. The insulation should be completed tomorrow or Friday.

Time 0.6

07-07-15	Permit 2014-89, 12 Baynes Road. I completed the final rough inspection for the plumbing, pressure tested, and the electrical.

Time 0.5

07-09-15	Permit 2014-89, 12 Baynes Road. I did the final inspection of the insulation and fire stopping on the second floor, attic, and garage. Unless there any changes all that needs to be done is the final inspection.

Time 0.7

08-18-15	Permit 2014-89, 12 Baynes Road. Inspected the propane line and electrical for the gas fireplace in the dining area. Looked okay. Did a partial walk through downstairs as most of it is painted and trim installed.

Time 0.7

10-09-15	Permit 2014-89, 12 Baynes Road. Jim called for me to do a inspection for a TCO. The plumber didn't get there to get the kitchen and bathroom ready. They were still working on the outside and inside electrical fixtures.

He wanted me to come Saturday and I could if the work was completed. Emailed Jim and set it up for Monday.

Time 0.7

10-12-15	Permit 2014-89, 12 Baynes Road. One bathroom is all completed, the kitchen is all completed except for the range hood that was damaged and a new one is being shipped. All the bedrooms are completed as well as all the other rooms except the two upstairs bathrooms. The gas fireplace needs closed in and ceramic tile installed (safe to use). There are a few ceiling fixtures that haven't arrived yet. The siding is almost finished except the upper section of the front of the house. All outside electrical fixtures are installed and plumbing fixtures. I will issue a 30 day temporary Certificate of Occupancy.

Time 0.4

11-24-15	Permit 2014-89, 12 Baynes Road. James emailed me and we set up a time to do the final inspection so I could issue the Certificate of Occupancy. Only thing was the pipe for the water heater's relief valve had the adapter installed and the copper pipe on the floor and wasn't installed. He will have the plumber take care of it. I will issue the CO.

Time 0.6

David H Lersch

Plainfield Building Inspector