Ian Rogers

PO Box 151

504-4912

Permit # 2013-20

Map/Lot 259/31.1

1306 Route 12A

Log home 27x37

02-27-13	Received emails from Ian Rogers about his building a log cabin and to set up a time to get together. We will do it 0n 3/5 at 5:30PM.

03-05-13	Permit 2013-20, 1306 Route 12A. I met with Ian to go over his plans for a log home on 12A. Plans looked okay, I told him to ask about egress windows for the bedrooms. He is planning on a full basement with a bulkhead for exit/entry to basement.

Time 0.6

06-26-13	Permit 2013-20, 1306 Route 12A. Dan Lapan called to have me inspect the footer forms. Rebar and ground wire installed, gave the okay to pour as well as answered Ian’s email that it was okay to pour.

Time 0.4

07-02-13	Permit 2013-20, 1306 Route 12A. I inspected the wall forms for the foundation. Looked okay and told Dan he could pour.

Time 0.5

07-09-13	Permit 2013-20, 1306 Route 12A. I inspected the perimeter drains and the blue foam insulation for the foundation. I told them they could backfill.

They were digging the trench and laying the water line.

Time 0.5

07-11-13	Permit 2013-20, 1306 Route 12A. I inspected the trench from the utility pole to the pedestal with the meter and main electrical panel including the conduit and the trench and conduit almost to the house location so they could backfill as a large section of it is in the middle of the driveway.

Time 0.3

08-21-13	Permit 2013-20, 1306 Route 12A. Inspected the log house and the second floor framing and rafters. Looked okay. No electrical wiring done yet but the framed walls will be sprayed foam and possibly the rafters. I will do a insulation inspection along with the electrical.

Time 0.6

09-09-13	Permit 2013-20, 1306 Route 12A. I inspected the rough in electrical wiring for the first and second floors. Looked okay and they would be spraying the foam insulation on the second floor.

Time 0.5

09-19-13	Permit 2013-20, 1306 Route 12A. I inspected the foam insulation and it looked good. It didn’t contain any voids and had sufficient thickness.

Time 0.3

10-19-13	Permit 2013-20, 1306 Route 12A. I inspected the rough in electrical plumbing and the rest of the rough in electrical wiring. Looked okay. I left a note for Ian stating that the holes in the plates needed to be fire stopped and I told him that the interior walls should have some fire protection as the walls are v-boards without any sheetrock installed on all the walls that are not logs. I told him when he called that there is a flame retardant coating you can put on after it is stained and/or coated with a clear finish.

Time 0.4

01-17-14	Permit 2013-20, 1306 Route 12A. Email to Ian in response to his email.

Ian,

Kitchen, bathrooms must be operational. All switches/receptacles installed and with wall plates. Smoke detectors installed and working.

Safe to live in. I am out of town and I have a backup to do the final inspection when you are ready. After he lets me know the house is

ready to occupy, I will issue the Certificate of Occupancy. What I will do is print it here, sign it and email it to you. The original

I will mail to the Town Hall along with others for Michelle to mail out.

... I went and did a final inspection of Ian Rogers new house and it's all set to receive a CO.

David H Lersch

Plainfield Building Inspector