Anne Rogers

141 True Road

Meriden, NH 03770

455-2041

Permit # 2013-57

Map/ID #  214/9

7.5KW pole mounted solar, perimeter drain work, bulkhead entry

10-17-13	Permit 2013-57, 141 True Road. Inspected the trench with conduit installed on a bed of sand for the cables from the solar array to the house. Looked okay, they had several loads of sand to cover conduit.

Time 0.3

10-19-13	Permit 2013-57, 141 True Road. Inspected the footer for the bulkhead entrance to the basement and the pictures they took with the rebar installed as I let the pour as I was unavailable. It looked okay. Trench filled in.

Time 0.8

10-30-13	Permit 2013-57, 141 True Road. I inspected the foam block wall forms and the installed rebar for the new bulkhead entry. It looked okay. The drain work was being worked on when I was there. Stone and drain pipes along the breezeway between the garage and house and along the rear of the house. The ground was sloped away from the house as well.

Time 0.5

David H Lersch

Plainfield Building Inspector