Jill Feen

4 Cedar Wood LN #306

Lebanon 03766

304-6598

Permit # 2017-07

Map/ID #  260/15

Siding house and garage

New windows, roof, front entrance, support beams kitchen/living area

Later added plumbing and electrical

09-13-17	Permit 2017-07, 147 Dodge Road. I received a call and email from Jill to do an inspection. House renovation almost finished. I told them the issues of what I could see there are several issues and concerns about what I can't see. A copy of the letter I sent to them after having completed my initial inspection is pasted to this report.

Time 1.1

Date:09-14-17

Reference: Inspection of house at 147 Dodge Road, Plainfield, NH 03781 for Permit 2017-07

At your request I inspected the house that is being renovated. No inspections were requested prior, during the renovation. Permit was for new siding, windows, roof, front door and the addition of support beams in the living/kitchen area. It also included siding on the garage, which has not been started. All new electrical wiring and plumbing was not part of the original permit. Since the interior is almost completed and sheathing on the outside, I could only inspect areas that were open for inspection.

Preliminary findings were as follows:

1.	Plumbing and electrical penetrations in floor plate were not fire stopped, I did not 	inspect 	the penetrations in the top plate.

2.	No smoke or CO detectors installed yet.

3.	The three bedroom windows did not meet egress code. (only one window per bedroom 	required)

4.	Receptacle spacing did not meet the required six feet to an outlet and some walls did not have a receptacle.

5.	Kitchen only had one of the two required GFI circuits and did not meet the required 	number of outlets and spacing. Outlets need to be reached with a two foot cord for 	counter tops and counters of two feet or more require an outlet.

6.	Outlets need to be child proof receptacles.

7.	Panel did not contain the required ARC fault breakers.

8.	Picture of wall insulation meets the energy code for the walls, need to verify the 	insulation in the ceiling has and R-factor of 49.

Questions I still have:

1.	Were the original outlet and switch electrical boxes still installed, just new devices and 	wire. If they weren't replaced by the proper size box, the would have to be replaced.

2.	Electrical code requires six inches of wire in the electrical box so replacing a device can be done safely.

3.	Proper vents for the plumbing.

The preliminary findings will need to be corrected and the above questions answered and verified by inspection before a Certificate of Occupancy can be issues, assuming the remaining work for the renovation of the house is completed.

If I can be of further help or answer any questions please don't hesitate to contact me.

11-04-17	Permit 2017-07, 147 Dodge Road. Met with home owners and their 			attorney Brad Wilder. They had installed detectors but did not have them 			linked together as per code. The windows are still there and they say they 			meet code since the two panes can un latched and tilted in and pushed to 			the sill 	allowing over six square feet. Replaced the outlets with child proof 		outlets. Verified new electrical boxes were installed when the work was 			completed. Penetrations were fire stopped by foam. Items 1, 6, 8 have 			been addressed. Questions answered by inspection and letter from 				contractor. Had letters from plumber and electrician stating everything 			was done according to code. I said it was not and spent considerable time 			copying pages from the IRC, etc. and scanning them to an email to Brad, 			Jill, and Steve H. They also stated ARC circuit breakers due to HB85, 			showed me a copy and I said I would look into it. A Copy of the bill was 			sent in email also. Only in case of a ARC breaker tripping regularly and 			no fault in wiring can it be temporary removed until the manufacturer can 			find resolution. Reports must be filled. I also sent message to State Fire 			Marshall's office to give me help on the egress window issue. The opening 		according to codes says clear opening, no special knowledge and for a 			child to open bottom sash, release tabs, tilt window in, rotate to remove 			sash and then do the same for the upper sash to give the required clear 			opening. A copy of the letters, my email and other documents will be in 			the town files.

Time 1.5 Meeting/Inspection

Time 2.6 Generating email, letter, scanning documents

11-20-17	Permit 2017-07, 147 Dodge Road. After sending emails to Brad Wilder with pages from the IRC, the owners agreed to install arc fault breakers, connect smoke detectors together, add additional circuits. The windows do not meet egress code as the contractor said in his letter. Steve and I sent separate emails to Brad stating that no completion of the permit stating that they met code would be issued without installing egress windows in the bedrooms. I checked with a local building supply and they could order a egress hinged window that would fit in the current rough opening and notified Brad via email. The town requires egress windows if new construction windows are installed when other work is being done allowing the rough opening to be enlarged to meet code. No additional inspections have been completed since the agreement to do the work required for completion except egress windows. Since egress windows will not be installed, this status of this permit is closed without a Certificate of Completion.

David H Lersch

Plainfield Building Inspector