Donald and Roberta Garfield

155 Main Street

469-3485

Permit # 2015-15

Map/Lot 102/19

Upfit barn

05-08-15	Permit 2015-15, 155 Main Street. brad called to have me inspect the 			drainage trench and we discussed the rest of the project. He had new stone 		in the lower part of the barn and was leveling it. He is waiting on 				structural information to see what they needed to support the main beam 			and upper floor.

Time 0.6

06-12-15	Permit 2015-15, 155 Main Street. Brad called to have me inspect the footer forms for the new rear wall and the forms for the posts that will support the new steel beam that is installed and temporary braced.

Time 0.3.

06-23-15	Permit 2015-15, 155 Main Street. Inspected the rear wall that used foam blocks, the drainage pipe along the rear of the barn and the trench with drain pipe installed. I also inspected the concrete supports for the posts.

Time 0.4

06-30-15	Permit 2015-15, 155 Main Street. I inspected the rebar that was supported on bricks for the new floor. All tied together and tied to bent rebar that was installed in the frost wall. Steel posts were mounted to support the new steel beam. Posts were installed to support the headers over the garage doors. Look great.

Time 0.4

David H Lersch

Plainfield Building Inspector