Denise Poulin

157 Hayward Road

675-2440

Permit # 2017- 43

Map/Lot 260-31

two car garage

07-05-17	Permit-none, 157 Hayward Road. Met with home owner to go over his 			plans to build a two car garage. He wants to do a floating slab, but he 			wants to pour frost wall and floor at same time.

Time 0.5

07-14-17	Permit-applied, 157 Hayward Road. Met with owner at side. He showed 			me the concrete deck with pressure treated 4x4s in a crosshatch pattern 			with concrete in the squares and he wants to do the same for the garage 			floor. I told him as long as the floor concrete was at least four inches thick 			it would be okay. He did apply for a permit.

Time 0.5

07-05-17	Permit 2017-43,  157 Hayward Road. Met with home owner to inspect the 			garage slab forms. Rebar and wire mesh installed. Okay to pour concrete.

Time 0.3

10-24-17	Permit 2017-43, 157 Hayward Road. Inspected completed two car garage. 			No plumbing or electric.

Time 0.2

David H Lersch

Plainfield Building Inspector