Larry Wolkin

205 Grantham Mountain Road

Meriden

469-3651

Permit # 2012-51

Map/ID # 245/11

22x13 addition with basement

08-14-12	Permit 2012-51, 205 Grantham Mountain Road. Larry called to discuss the addition that was put on his house without a permit. He applied for one on 8-14-12. When I got there except for installing the windows, taping the sheetrock and paint/trim it was finished. Larry was supposed to have Peet call me. I will need a signed statement from the concrete contactor as to what and how he did the footer and foundation walls. I will also need signed statements from the plumber and electrician as to the work that was completed. Since I could only see what is exposed in the basement it will be impossible to issue a occupancy certificate with this information.

Time 1.1

09-11-12	Permit 2012-51, 205 Grantham Mountain Road. Peet called to have me inspect what has been completed. The windows were installed, additional insulation was put of the interior walls then the sheetrock which caused two of the electrical boxes not to be flush with the finished wall. The relief valve on the hot water tank needs to be piped to within four inches of the floor. Since the foundation wasn’t insulated on the outside, Peet will have to apply insulation to the inside of the basement wall as it is heated space. I received a copy of the email from the concrete contractor with the footer and wall specifications. When the new panel is in place, I will meet with the electrician.

Time 0.9

09-14-12	Permit 2012-51, 205 Grantham Mountain Road. Peet called and said the electrician was done. I inspected the electrical and it was okay. Peet was almost finished with insulation the basement and bulkhead. He still needed to install hand rails on the basement stairs and the relief valve wasn’t installed yet.

Time 0.6

David H Lersch

Plainfield Building Inspector