Charles and Holly Newton

213 Old County Road

667-5827

Permit # 2016-10

Map/Lot 217/1

28x50 modular home

03-03-16	Talked to Michael Wood about new modular home that will built. He 			needed information about snow load and wind speed and needed a letter

stating town requirements. Generated letter and emailed to him and also 			gave a copy to Steve to have at the town hall and put on the web.

802-353-5909, wooddevco@yahoo.com.

Time 0.5

04-26-16	Permit 2016-10,213 Old County Road. Inspected the utility pedestal with the meter panel with a 200 ampere disconnect and the temporary sub panel to provide temporary power during construction. I will email Eversource.

Time 0.8

04-29-16	Permit 2016-10, 213 Old County Road. I inspected the footer forms with ground wire installed. Rebar supported by string. Okay to pour.

Time 0.5

05-05-16	Permit 2016-10, 213 Old County Road. Inspected the foam block wall forms with rebar installed on every row. Okay to pour.

Time 0.5

05-10-16	Permit 2016-10, 213 Old County Road. Inspected the plumbing in the basement floor for a bathroom. Looked okay and let Michael he could pour.

Time 0.5

06-21-16	Permit 2016-10, 213 Old County Road. Inspected the buried electrical service entrance including the electric panel, junction box. Needs a longer cable from the junction box outside that connects the cable from the meter panel to the house circuit panel as the cable that came with the house assumed the entrance was on that end and since the entrance was changed to the other end of the house the two cables are temporary spliced together.

Time 0.5

07-12-16	Permit 2016-10, 213 Old County Road. Steve left me a message about perimeter drains not going to daylight. Went to house, they have cut a a driveway around the left side and across the back of the house. Contractor showed me where the drains end on either side of the entrance to the basement. They will be connected and go back to the bank to daylight as he needs to dig a trench as well as dig along the edge of the basement floor  where the slab is exposed. He was waiting until the driveway around the house was completed. I also walked through the house, they are getting close. I also let them know that until the rear deck is built, the sliding door will have to be secured so there is no chance of opening it.

Time 0.7

10-04-16	Permit 2016-10, 213 Old County Road. Went by to see if they were ready for the final inspection as last time in July they were getting close. The driveway at the rear of the house was completed and a deck was being built on the rear and the right end of the house. I knocked on the door and finally Holly came to the door. She works nights, apologized for getting her up and told her that they shouldn't be living in the house without an Occupancy Permit. She said she would have Charlie call me.

Note: as of 10-11 no call.

Time 0.3

06-30-17	Permit 2016-10, 213 Old County Road. Letter sent 05-30-17, no response. Closed permit without CO.

09-21-17	Letter sent requiring a CO.

David H Lersch

Plainfield Building Inspector