Jeffrey Clouse

238 Ladieu Road

267-349-9266

Permit # 2017-77

Map/Lot 224/12

new kitchen cabinets/bathroom fixtures with some

electrical and plumbing

12-06-17	Permit 2017-77, 238 Ladieu Road. received a call from Jeff to have the kitchen rough in inspected, asked me to talk to plumber. Called Brad to give him information.

12-07-17	Talked to Andy the plumber. He removed the vent pipe that was under the floor, not code, and installed a vent that will be under the sink counter, no plumbing upstairs. Brad said there were holes in the sheetrock when he inspected and noticed bathroom on the other side of the wall had the fixtures removed and work going on there. Talked to Jeff and let him know that the penetrations in the plate need to be fire stopped and the holes in the sheetrock need to be closed up.

Time 0.6

- 12-07-17	Permit 2017-77, 238 Ladieu Road – Kitchen Pre-cabinet electrical and plumbing 				rough-in. Met owner on-site. Kitchen walls very cut-up. State of both electrical 				and plumbing raised several questions. Owner called plumber who was able to 				describe plan (included removing legacy sink dwv) I noted need to firestop 				penetrations in plates. Electrician unavailable to answer electrical questions. 				Owner to take pictures and send to Dave Deferred to Dave re: approval.

12-07-17	Permit 2017-77, 238 Ladieu Road. Jeff sent me pictures of the holes fire stopped and they replaced the bottom three feet of the sheetrock in the kitchen. Looked good and told him he could install cabinets. I also asked him about the bathroom the wasn't on the permit. He will call when all the rough in is completed.

Time 0.2

12-19-17	Permit 2017-77, 238 Ladieu Road. Received a text from Jeff in answer to my text about the tub plumbing. He gave me the phone number for Randy, plumber, 267-349-9266. I called and told him of the issue Brad had of the flex pipe on the drain and that it was only 1-1/2 inch pipe. Pipe okay for tub but flex needs to go. He said he would have his guy make sure it was to code and send me pictures of the fix. Didn't get pictures, sent Jeff a text that I didn't get pictures as promised and if not I would have to have Brad inspect. Jeff wants it done right. Haven't heard back as of 12-23.

Time 0.3

12-23-17	Permit 2017-77, 238 Ladieu Road. Sent text to Jeff both yesterday and today. I will send Brad to inspect if I don't hear back or receive pictures.

Time 0.1

01-22-18	Permit 2017-77, 238 Ladieu Road. Sent texts to Jeff, reply from Jeff and Plumber Randy. Sent pictures of vent pipe for tub plumbing. Need picture of plumbing for drain as had flex pipe. Left word for Brad to check the plumbing. Randy said he would send pictures of under the installed tub, has an access panel d0wnstairs.

Time 0.2

01-26-18	Permit 2017-77, 238 Ladieu Road. Talked Jeff as he wanted to know if the plumber Randy got with me. We also sent text before he called me. Question I had was the tub drain that had the flex drain pipe. Jeff said it is all PVC plumbing now. I also asked Brad to verify. He  didn't find the access panel down stairs but what he saw looked okay. He didn't look in front of the tub where Jeff said you could see the plumbing. Told Jeff to continue and let me know when finished and that Brad would be stopping by again.

Time 0.2

07-12-18	Permit 2017-77, 238 Ladieu Road. I inspected the finished kitchen where new cabinets and counters were installed, there was some new plumbing and all holes were fire stopped. The also remodeled both bathrooms with new fixtures. I will issue a Completion Certificate.

Time 0.7

David H Lersch

Plainfield Building Inspector