Kathleen Marshall

PO Box 234

Meriden, NH 03770

Permit # 2010-54

Map/ID # 224/11

8x12 sunroom and landing with steps

258 Ladieu Road

09-22-10	Permit 2010-54, 258 Ladieu Road. I inspected the sonatubes with rebar installed for the new sunroom section. Wesley will be putting plywood on the underside of the joists and foam insulation between that and the pressure treated plywood flooring for the sunroom.

Time 0.8

10-27-10	Permit 2010-54, 258 Ladieu Road. I did the framing inspection for the sunroom and the small deck with steps at the entrance. He will call for the rough in electrical and he is planning on insulating the walls even though the room isn’t heated.

Time 0.5

11-01-10	Permit 2010-54, 258 Ladieu Road. I inspected the rough in wiring in the sunroom. Looked okay and I told them to call when it is finished. They were also finishing up the outside siding.

Time 0.3

05-30-13	Permit 2010-54, 258 Ladieu Road. Kathleen called after receiving my letter regarding the final inspection of the sunroom. I did the final inspection and will issue a certificate of completion.

Time 0.5

David H Lersch

Plainfield Building Inspector