Patricia Aiken (Trustee)

PO Box 117

Cornish Flat, NH 03746

469-3815

Permit # 2016-67

Permit # 2017-71

Map/Lot 224/11

renovate portions of house and add a 24x32 addition

258 Ladieu Road

09-26-16	Permit 2016-67, 258 Ladieu Road. I met with Brian to go over plans for the house. The kitchen area will stay the same but the bedrooms, bathrooms, and pantry will be changed. The hall will be made wider and the no complaint basement stairs will be removed and be reconstructed in the new 24x32 addition which will house the two bedrooms that were in the old house.

Time 0.8

10-11-16	Permit 2016-67, 258 Ladieu Road. Dave called to have me inspect the floating slab for the addition of the two car garage. Looked okay. Also discussed the addition to the house as all the excavation was completed. He will be doing the footer and will call when he is ready for inspection. They will be using foam block construction for the wall which will give an R23 value for insulation.

Time 0.5

10-12-16	Permit 2016-67, 258 Ladieu Road. Dave called to have me inspect the footer forms with rebar and ground wire installed. Okay to pour.

Time 0.4

10-20-16	Permit 2016-67, 258 Ladieu Road. Dave called and said the foundation foam blocks were in place with rebar. Also drilled holes in foundation to install rebar to connect addition foundation wall to house foundation.

Time 0.7

03-28-17	Permit 2016-67, 258 Ladieu Road. Met with Dan Michaud 558-4005 and inspected the framing that has been completed. We went over project and he will call if any questions and will let me know when he is ready for any inspections. A new service entrance panel installed with Kohler generator and transfer switch. Old panel is still being used and new wiring will be installed to new panel and old panel removed.

Time 0.7

05-23-17	Permit 2016-67, 258 Ladieu Road. Charlie called to have me inspect the rough in electrical wiring and to go over plans to insulate some of the new addition's basement. I also inspected some of the new wiring (replacing all electrical wiring) and some of the rough in plumbing. Discussed the chimney flues that supported wood stoves that will not be used. I told him to seal off the one upstairs with cement as it is the same flue as the downstairs wood stove that will be replaced with a propane stove.

Time 1.4

06-05-17	Permit 2016-67, 258 Ladieu Road. Had an appointment to inspect the 			rough in electrical. Was late getting there, no one there, scheduled for next 		day.

Time 0.5

06-06-17	Permit 2016-67, 258 Ladieu Road. Met with Johnny, the electrician, 			inspected the new panels, most all of the old circuits have been replaced. 			Looked okay and said they could insulate..

Time 0.8

10-23-17	Permit 2017-71, 258 Ladieu Road. Was supposed to meet Charlie on 			Saturday but forgot, stopped by to see progress. Attic insulated by blown 			in and foam hoods around LED canned lights. Headers were sprayed foam 		as well as the walls. Sheetrock installed, siding being installed, and 			flooring installed. Contractor said it probably will be spring when 				everything is finished. Charlie may want to move in before everything was 		finished and I told them the requirements for a Temporary CO.

Time 0.6

David H Lersch

Plainfield Building Inspector