John Friedman

268 Porter Road

709-2008

Permit # 2017-42

Map/Lot

14kw generator

02-20-18	Permit  2017-42, 268 Porter Road – Tuesday (Freidman?) Met owner on-			site to inspect back-up generator. (Kohler, propane) – unit is pad mounted 			with wiring run underground to exterior disconnect mounted on the side of 		the house. The risers on either end of the underground are protected (weed 		wacker) with pvc sleeves. The transfer switch is mounted next to house 			load center. Both disconnects are clearly labeled and the installation is 			neat and solid.

02-25-18	Permit 2017-42, 268 Porter Road. Received Brad's report of generator 			installation and will issue a Certificate of Completion.

Time 0.2

David H Lersch

Plainfield Building Inspector