29 Spruce Park

Permit #

Map/Lot

Repair water damaged OSB, replace windows and siding.

07-23-09	The manufactured home across the road from me was having new siding and windows installed. Some of the OSB board was wet and soft and was being replaced. they are putting a vapor barrier, foam insulation, then the new vinyl siding. No one applied for a permit and I said that since there is repairs being done and replacement of windows that they should have gotten one. I checked the windows and they were two small for egress in the two bedrooms. The workers weren’t too happy after we measured the openings. The contractor arrived later and I let him know what was required after researching the codes for manufactured homes and egress windows. The contractor had no clue about egress requirements. He said he would just have to eat the cost of the two windows and get new ones. He came in later and said that his dealer said they were egress. I told him I needed a letter or document from the manufacturer stating that model and size met the egress requirement.

Time 1.0

07-24-09	Spruce Park

I researched on line for Harvey slim line windows and found out that the height required was 58 inches to be egress compliant and they were several inches too short. I found out that the contractor had ordered larger windows today. I will make sure work is done according to code.

Time 0.7

David H Lersch

Plainfield Building Inspector