Gabe & Hayley Giacomo

375 Freeman Road

307-631-7926

Permit # 2019-10

Map/Lot 239/7

finish basement

03-07-19	Permit 2019-10, 375 Freeman Road: Electrical/Plumb Rough-in. 			Met Peet onsite. Reviewed work to enable exterior wall spray 			insulation. Noted ext wall sheathing dampness (can effect foam 			expansion and adhesion). Peet indicated he had used a heater to 			dry it. He thought it would be ok. Electric and plumbing rough-in ok. 			Toilet will have macerator & 1.5 drain (confirmed unit spec on-			line later). Gave ok to proceed with spray insulation.

David H Lersch

Plainfield Building Inspector