Todd Milo Sr. & Patty Spencer

16 Westgate Road

675-5571

Permit # 2014-27

Map/ID #  108/20.2

30x48 SFH w/att/28x28 garage

40.5 Hayward Road

07-10-14	Permit 2014-27, 40.5 Hayward Road. I inspected the footer forms for the house and it was okay and I told them they could pour.

Time 0.3

07-15-14	Permit 2014-27, 40.5 Hayward Road. I inspected the foundation wall forms, they were okay and I told them they could order the concrete.

Time 0.2

07-23-14	07-24-14 Telephone calls regarding 62 Pierce Road, 241 Freeman Road, 40.5 Hayward Road and 288 Platt Road.

Time 0.5

07-29-14	Permit 2014-27, 40.5 Hayward Road. Inspected the basement floor insulation and let them know that they needed r-10 along the walk out basement wall. Foundation was coated and backfilled. Basement walls will be insulated on the inside.

Time 0.3

09-19-14	Permit 2014-27, 40.5 Hayward Road. Went to inspect the buried service entrance and they were not ready. Said should be ready by noon.

Time 0.3

09-19-14	Permit 2014-27, 40.5 Hayward Road. Inspected the trench and conduit for the electrical service. All was okay and I will notify PSNH that it is okay to connect service.

Time 0.8

10-17-14	Permit 2014-27, 40.5 Hayward Road. I did the rough in electrical and plumbing inspection so they could spray the insulation. Looked good.

Time 1.0

10-29-14	Permit 2014-27, 40.5 Hayward Road. I inspected the sprayed insulation. Only found one small area that needed more insulation, didn't get in the corner.

Time 0.5

05-26-15	Permit 2014-27, 40.5 Hayward Road. I did the final inspection with the owner, electrician, plumber, general contractor Bernie. I will issue a Certificate of Occupancy

Time 0.7

David H Lersch

Plainfield Building Inspector