Andrea Storn

44 West 77th Street

NY 10024

917-783-0050

Permit # 2017-21

Map/Lot 104/17

renovate house

42 Camp Road

05-02-`7	Permit 2017-21, 42 Camp Road. Met with contractor to go over 				renovation plans for the house. Maybe a spiral staircase from the lower 			level to the loft, replacing stairs from the lower level to main level and the 			ladder to the loft. The area could be used for a main floor bathroom. They 			want to open the downstairs to enlarge the bedroom and needs to check 			the to see if the beams can support the load once the center wall comes 			out. He has to remove some sheetrock and trim to expose the beams over 			the walls.

Time 0.8

07-23-17	Permit 2017-21, 42 Camp Road. I inspected the electrical wiring in part of 		the house that is between the house and garage/barn. Also some external 			wiring for lights in the new roof over the rear entrance to the house as they 		want to close in the ceiling.

Time 0.7

08-01-17	Permit 2017-21, 42 Camp Road. Jim called to have me inspect the rough 			in electrical, rough in plumbing almost ready for inspection. Electrical 			okay, penetrations in fire stopped, noticed radiant heat pipes coming out of 		floor. Contractor said they had pipes installed over two inches of 				insulation and poured a new concrete floor. I let him know I should have 			inspected the pipes as well as the insulation. They poured over the existing 		floor that had insulation under it. Two inches of foam against the 				foundation was already there plus two inches of foam insulation from the 			foundation wall, underground, going away from the building for two to 			four feet.

Time 1.2

08-03-17	Permit 2017-21, 42 Camp Road. I inspected the rough in plumbing with Doug, pressurized and all okay. They will be insulation on Monday.

Time 0.8

08-06-17	Permit 2017-21, 42 Camp Road. Inspected the sprayed in foam insulation 			in the basement and on the first floor. Gable ends were still original 			fiberglass. Okay to cover.

Time 0.4

11-13-17	Permit 2017-21, 42 Camp Road. Jim O. called to have me do a final 			inspection of the electrical work. Everything was completed okay. 				Plumbing not finished yet but close. Needs to provide railing for the loft.

Time 0.7

01-04-18	Permit 2017-21, 42 Camp Road. Brad inspected the renovated house and other 				than the temporary step at the front entrance that will be replaced when the 				weather gets warmer and the small loft railing doesn't appear to meet the 200 				pound code, although it is the right height I will issue a completion certificate 				when I get Brad's report..

01-04-18	Permit 2017-21, 42 Camp Road. Final (temp cc?) Met Contractor Evan Dybvig on site, Walked through work areas. All electrical boxes, devices installed or blank covered.  Some light fixtures have utility grade porcelain open bulb fixtures. Is this ok? Railing in loft likely does not meet live load requirements (section/table 301.5 - 200 lbs in any direction to guardrail/handrail), based on section area, material, fastening of newel posts - your call. No easy way to modify to make compliant. Evan mentioned step at front door to be recycled concrete from Mak's. Installation delayed until spring.

Otherwise everything looked ok. BRAD

01-13-18	Permit 2017-21, 42 Camp Road. I will issue a Certificate of Completion 			stating renovation met code except for railing and the temporary front 			step.

David H Lersch

Plainfield Building Inspector