J

421 Willow Brook Road

6

Permit # 201

Map/ID #

Renovation after water/mold

02-12-14	Permit 2014-xx, 421 Willow Brook Road. I talked to contractor about the work that is going to be done after the house was gutted due to water and mold. Insurance company doesn't want to pay for any upgrades but according to Larry Davis the roof rafters are not large enough to support the snow load, there were skylights that were installed without a permit after talking to Michelle, wiring is a combination of old knob and tube, etc. and needs to be upgraded. A new panel was installed when the two car attached garage was built by Larry (NOTE: No inspections were preformed, letter sent, no response.) The exterior walls won't support the thickness needed for the new insulation, some are not even 2x4's. I asked Win to call Larry and do a walk and let me know what he thinks. I feel to be able to issue a CO it needs to be up to code. As of 2-21 Win hasn't got with Larry in response to my email yesterday as to status of inspections to date that I have requested.

Time 0.4

02-27-14	Permit 2014-xx, 421 Willow Brook Road. (Win) Meeting with contractor at 421 Willow Brook Rd.

Time 0.75

03-34-15	framing insp