Brandon William Latlaye

45 Porter Road

252-1781

Permit # 2017-49

Map/Lot 216/2.2

new sfh modular

06-19-17	Permit 2017-49, 45 Porter Road. Met with home owner to go over questions about the electrical trench as it will be aerial part way then buried. Covered depth, sand requirements, spacing between low voltage conduit and power conduit. Also covered footer requirements.

Time 1.0

06-27-17	Permit 2017-49, 45 Porter Road. I inspected the trench with the conduit installed, good base of sand, 3 feet deep, gave the okay to backfill.

Time 0.5

08-18-17	Permit 2017-49, 45 Porter Road. I inspected the footer forms for the modular home. Looked good, rebar supported, bent around corners, tied together, center supports not pads but a footer through the center. Contractor ordered tie down strips that some modular home manufacturers require on the four corners. House corners tied to foundation wall. Okay to pour.

Time 0.8

08-18-17

David H Lersch

Plainfield Building Inspector