s

45 Porter Road

4

Permit # 2017-

Map/Lot

new sfh

06-19-17	Permit 2017-xx, 45 Porter Road. Met with home owner to go over questions about the electrical trench as it will be aerial part way then buried. Covered depth, sand requirements, spacing between low voltage conduit and power conduit. Also covered footer requirements.

Time 1.0

06-27-17	Permit 2017-xx, 45 Porter Road. I inspected the trench with the conduit installed, good base of sand, 3 feet deep, gave the okay to backfill.

Time 0.5

David H Lersch

Plainfield Building Inspector