Marc Hampers & Tracy Hauck

50 Eaton Road

448-9212

Permit # 2017-22

Map/Lot 227/15

Studio/man cave separate structure

05-18-17	Permit 2017-22, 50 Eaton Road. I inspected the footer forms with rebar for the frost wall for the new building. Two rows of rebar and vertical L shaped rebar tied to horizontal rebar. Looked okay.

Time 1.0

05-22-17	Permit 2017-22, 50 Eaton Road. I inspected the wall forms for the frost wall. Looked okay.

Time 0.7

08-14-17	Permit 2017-22, 50 Eaton Road. I did the rough in plumbing and electrical inspection, okay, told them to make sure penetrations are fire stopped.

Time 0.4

08-15-17	Permit 2017-22, 50 Eaton Road. I inspected about half of the blown in insulation, fabric was installed over most of the building, but not all filled. They wanted to install sheathing on the cathedral sections gable end. THey fire stopped holes. The rest should be done Friday as the sheetrock installers are coming.

Time 0.7

08-18-17	Permit 2017-22, 50 Eaton Road. Inspected the balance of the blown in insulation including the fiberglass installed over the header. Okay to sheetrock.

Time .07

09-13-17	Permit 2017-22, 50 Eaton Road. I inspected the trench for the water from the well and the electrical trench with conduit from the transformer pad to the meter panel on the right side of the building. No wires pulled yet.

Time 0.7

11-01-17	Permit 2017-22, 50 Eaton Road. Received a call to do the final inspection for the studio/man cave. Tasco alarm system installed. Upstairs was an exercise room and office/den. First floor had a wood stove, a kitchen area, bathroom and lounge/game area. Very well done. I will issue a Certificate of Occupancy due its usage.

Time 0.6

David H Lersch

Plainfield Building Inspector