Mark Hardy

60 True Road

469-3223

Permit # 2017-67

Map/Lot 214/20

solar

12-19-17	Permit 2017-67, 60 True Road. Brad inspected the solar installation on 60 True Road. I will be emailed the form to sign for Liberty.

12-21-17	Permit 2017-67, 60 True Road. Received email with Liberty form to sign and return to solar company. Printed, signed, scanned and emailed back.

Time 0.2

12-19-17	Permit 2017-67, 60 True Road – Hardy – Solar system expansion. Met 			Owner and Installer rep on site. New array is located on garage roof 			(existing array is on house roof). Electrical conductors run from back side 			of panels to rake edge, along rake trim in rigid conduit transitioning to flex 		to clear cornice trim, back to rigid down corner board to disconnect 			enclosure and new “rec” meter. Meter on eave edge wall, but inside of 			drip line. Disconnect and meter are labeled clearly. Grounding visible 			inside and out. Everything neat and secure.

David H Lersch

Plainfield Building Inspector