Jesse and Ruth Stalker

62 Pierce Road

298-8913

Permit # 2014-47

Map/Lot 218/3

24x30 2 car garage with 2 bedroom apartment

08-15-14	Permit 2014-47, 62 Pierce Road. Inspected the footer forms. Rebar supported and tied together and ground wire clamped to rebar as required. Look good. They are going to put R10 under slab and R15 on the edge of the slab.

Time 0.7

08-21-14	Permit 2014-47, 62 Pierce Road. Inspected the wall forms for the garage with an upstairs apartment. Looked okay.

Time 0.5

09-19-14	Permit 2014-47, 62 Pierce Road. I inspected some of the framing and had concerns about how the joists were nailed to the beam and not on it. I have received emails from contractor with copies of certified letters of the design and other jobs that were completed. The time for that is not included but is included in reports/emails/codes. I emailed them to continue after reviewing the documents.

Time 0.5

10-14-14	Permit 2014-47, 62 Pierce Road. Did a framing inspection and discussed the separation of the garage area from the upstairs and the stairs going to the upstairs. they wanted solid wood doors and I said they should have a 1/2 hour fire rating both for the door and the walls and ceiling. If the door was coated with a fire retardant that would meet the 1/2 hour that would be okay.

Time 0.6

11-05-14	Permit 2014-47, 62 Pierce Road. Inspected the rough in electrical wiring and plumbing. Looked okay.

Time 0.7

11-10/14	Permit 2014-47, 62 Pierce Road. I inspected the new electrical service main circuit panel and some additional rough in electrical. Looked good.

Time 0.4

11-19-14	Permit 2014-47, 62 Pierce Road. Win did the insulation inspection. OK to cover with sheetrock.

Time 0.45

David H Lersch

Plainfield Building Inspector