Jodie Bastian

66 Carvel Lane

675-2474

Permit # 2011-42

Map/Lot #258/22

15x20 addition to kitchen and new dining area.

10-07-11	Permit 2011-42, 66 Carvel Lane. Inspected the footer forms for the addition. Looked okay and told him he could pour and to call when the wall forms were ready.

Time 0.7

10-31-11	Permit 2011-42, 66 Carvel Lane. I was out of town when the walls forms were ready to inspect, so I told him to pour unless he heard otherwise from me. I inspected the frost wall that was insulated and ready to backfill. Kevin Mac called and due to the ledge there isn’t anyway to put in a perimeter drain. He said with all the rain, there isn’t any water around the foundation and asked if he could just put in gravel and sand. I told him it was okay.

Time 0.3

11-15-11	Permit 2011-42, 66 Carvel Lane. I was called to inspect the trench for the buried utilities. The original power was direct buried and is being replaced with new cable in conduit. Several areas of ledge were removed and a sand base was under the conduit. Looked okay and told them they could backfill. PSNH will be coming by as well to inspect.

Time 0.6

12-13-11	Permit 2011-42, 66 Carvel Lane. I inspected the rough in wiring, looked okay.

Time 0.3

12-14-11	Permit 2011-42, 66 Carvel Lane. Inspected the insulation so they could sheetrock. Looked okay.

Time 0.5

David H Lersch

Plainfield Building Inspector