Chad & Trina Rogers

672 Willow Brook Road

252-1402

Permit # 2012-40

Permit # 2013-14

Map/Lot 215/5

23’8x40 Modular home

06-26-13	Permit 2013-14, 672 Willow Brook Road. I inspected the footer forms with ground wire and rebar installed. I gave the okay to pour.

Time 0.5

07-09-13	Permit 2013-14, 672 Willow Brook Road. I inspected the foundation wall forms, not completely finished but enough for me to okay so he could order concrete.

Time 0.8

07-19-13	Permit 2013-14, 672 Willow Brook Road. I went by to see how things were going. It was backfilled and blue foam was only installed to ground level leaving about 3-4 feet of foundation un-insulated. I will talk to Chad.

Time 0.6

07-22-13	Permit 2013-14, 672 Willow Brook Road. I met Chad at the site and I talked about the insulation. He will be finishing the basement and I told him he could insulate inside as he is going to stone the exposed foundation wall and adding the foam on the outside would cause a problem for him. He said there was foundation sealer as I didn’t see before it was backfilled and he said that there were perimeter drains installed both inside and outside the foundation. The house was there and will be set Thursday and Friday and Johanna will install the panels and electric meter on Monday for me to inspect and notify NH-Co-Op. The inside of the home needs to have sheetrock installed as Chad is going to do it.

Time 1.0

07-29-13	Permit 2013-14, 672 Willow Brook Road. Johanna wanted me to inspect the service entrance for the new home. She was still installing conduit up the side of the house, but the meter panel was installed with main breaker as per NH electric.

Time 0.6

07-31-13	Permit 2013-14, 672 Willow Brook Road. I went to inspect the service entrance and all was okay. The circuit panel was installed and operational. I also inspected the main drain pipe outside to the septic so they could backfill the trench. The propane hot water boiler/hot water tank was being installed. It was mounted and vented, hot water baseboard pipes were being installed and connected to heating manifolds.

Time 0.9

08-06-13	Permit 2013-14, 672 Willow Brook Road. I inspected Johanna’s electrical work and it was okay. The wall mounted boiler needs a discharge pipe on the backflow valve and I need to verify that a relief valve is installed and correctly. All the heating pipes are installed except the second floor which is unfinished. There is still some joists that were damaged and need to be shored up. Also it looks like someone is living in the house and I need to call Chad about that and the boiler. The second floor will be done by homeowner and I need to make sure it is done correctly.

Time 0.6

09-08-13	Permit 2013-14, 672 Willow Brook Road. Chad asked me to inspect the rough in electrical wiring on the second floor. He was going to do it himself, but had Emily Electric do it. I asked him if he was living in the home and he said yes. I told him he should have a Occupancy Permit prior to occupying the house. I went by and as I found out later he had to go out of town, so I will do it tomorrow.

Time 0.7

09-09-13	Permit 2013-14, 672 Willow Brook Road. I went and inspected the rough in wring and it was okay. I also did a walk through inspection and everything looked good. I will issue a 90 day Temporary Certificate of Occupancy.

Time 0.8

10-01-13	Permit 2013-14, 672 Willow Brook Road. Inspected the second floor insulation so the sheetrock could be installed. More than enough insulation to meet code.

Time 0.8

David H Lersch

Plainfield Building Inspector