Singing Hills

71 King Drive

469-3236

Permit # 2009-74

Map/Lot 245/24

Pavilion

06-04-10	Permit 2009-74, 71 King Drive. I inspected the seventeen holes with the tubes in place, four feet deep with gravel at the bottom.

Time 0.1

06-09-10	Permit 2009-74, 71 King Drive. Inspected the framing for the raised platform for the pavilion and it was okay. The work is being done by Biebel Builders.

Time 0.1

06-11-10	Permit 2009-74, 71 King Drive. I inspected the platform with the 5/4x6 decking installed and it was okay. The one side and end will have the required railing as the one corner is over 30 inches high. They also enclosed the side and end with paneling from the platform to the ground. The other side and end are above ground level the width of the headers.

Time 0.1

06-30-10	Permit 2009-74, 71 King Drive. Biebel Builders put up the side and end walls of the pavilion that were build in panels at their shop. They installed siding boards above the window and door openings and on the gable ends. The window openings are for screens. The pavilion will be centered on the platform with open decks at each end.

Time 0.1

07-13-10	Permit 2009-74, 71 King Drive. Met with Paul Biebel to go over placement of electrical panel. It was in a corner on the inside of the pavilion and about three inches from the floor. I suggested putting it on the corner diagonally opposite and on the outside as it would be at least three feet from the ground. We decided on a location under the enclosed platform just below where I suggested and he will have his crew make an access panel. The roof is completed and the screen windows are installed. I will inspect the wiring when I get back in two weeks. It should be finished by then.

Time 0.5

08-05-10	Permit 2009-74, 71 King Drive. The pavilion is almost finished. There are benches installed on both ends of the decks that work as the railings but under the seats, it is open so a child could crawl under the bench and fall off the deck. They will be closing it in. There are two fan/lights on the ceiling and the trench is being dug to connect power for them from the bathhouse. A sub panel is mounted under the deck with an access panel.

As soon as the electrical and the bench work is completed I will issue a completion certificate.

Time 0.2

David H Lersch

Plainfield Building Inspector