David Bae

79 True Road, Plainfield

PO Box 30, Meriden

607-351-8759

Permit # 2018-04

Map/Lot

new stairs, metal with wood steps

01-17-18		Call from contractor, 802-356-4383 about whether he need a permit to

replace the stairs. When he said he was changing stairs to open risers, I

told him to get a permit as it will have to be inspected. He will do

something to ensure the four inch in the riser opening. I said sometimes

metal rods were used.

Time 0.1

05-07-18	Permit 2018-04, 79 True Road. I inspected the new metal stairs going from the lower lever to the first and second floors. Steps were wooden planks mounted to risers, cable balusters were used, four inch between steps that I told them they needed earlier in a phone call was accomplished by a larger angle iron under the edge of the step. I will issue a Completion Certificate.

Time 0.4

David H Lersch

Plainfield Building Inspector