Rich & Camilla Baker

846 Route 12A

252-1575

Permit # 2017-41

Map/Lot 237/52

renovation and addition single to 2 story

08-11-17	Permit 2017-41, 846 Route 12A. Bernie sent me pictures of footer forms 			for the addition, looked okay and told him he could pour.

Time 0.1

08-14-17	Permit 2017-41, 846 Route 12A. Bernie called to have me inspect the 	addition wall forms. Okay

Time 0.6

09-29-17	Permit 2017-41, 846 Route 12A. Bernie called for an inspection of the footer forms for the rear addition. Looked okay. Did a walk through as some of the rough in electrical and plumbing was completed. Roof rafters were insulated with spray form.

Time 0.6

10-03-17	Permit 2017-41, 846 Route 12A. Call to inspect the frost wall forms for the breezeway and garage on the rear of the house. Looked okay. Rebar pinned to house foundation.

Time 0.3

10-09-17	Permit 2017-41, 846 Route 12A. Inspected the plumbing that will be under the slab for the breezeway, looked okay. He had two inches of foam for the walls and I said it had to be three, also he was going to put only two inches under the slab that will have radiant heat, needs to be three. He will call before pouring floor.

Time 0.4

10-11-17	Permit 2017-41, 846 Route 12A. Inspected the floor insulation and the radiant heat plumbing for the breezeway's floor. Okay to pour.

Time 0.6

- 12-01-17	Permit 2017-41, 846 Route 12-A – Electrical & Plumbing Rough-in. Met Bernie 				on site. Entry elec & Plumb rough-in s shower wet vented? (in-slab) otherwise all 				visible and looked good. Electrical plated as needed. Sunroom electrical looked 				good. Penetration for exterior light and outlet air sealed. Raised questions about 				existing stair rise/run (quite steep) and egress for existing “Basement” bedroom. 				Indicated that I would discuss w/Dave and he would respond to Bernie.

12-2-17	Permit 2017-41, 846 Route 12A Phone call with Brad about his inspections on 12-1-17  rough in plumbing and electrical in mud room-okay but some issues were found in the basement bedroom-no egress window and stairs very steep.

12-4-17	Permit 2017-41,846 Route 12A. Talked to Bernie about issues and told him he needed to install egress window in bedroom, I suggested an insert swing out egress hinge would fit in the opening, the stairs needed to come closer to code and he said because of head room he had some work with the beam and would find a solution.

Time 0.2

12-14-17	Permit 2017-41, 846 Route 12A. Bernie called as they were going to install an 1100cfm hood over the kitchen range. Had some concerns about make up air. I asked if they were going to put in air exchanger and he said yes, so that would provide intake air when the hood was running.

Time 0.1

04-19-18	Permit 2017-41, 846 Route 12A. Inspected the rough in electrical in the basement. Looked okay to insulate.

Time 0.3

10-31-18	Permit 2017-41, 846 Route 12A. Met with Bernie and did the final walk through. The entire single story house was renovated and a second story was added as well as an addition to the right front of the house. A heated breezeway was constructed on the back of the house to a the new attached two car garage that the rear of which butts against the existing detached garage. I will issue a certificate of completion.

Time 0.3

David H Lersch

Plainfield Building Inspector