David & Ellen Bonner

PO Box 530

Southport, Ct 06890

203-232-9061

Permit # 2015-49

Permit # 2017-26

Map/Lot 234/7

demo garage family room, rebuild

86 Columbus Jordan Road

10-16-15	Permit 2015-49, 86 Columbus Jordan Road. Lou Dirkse asked me to come buy and look at the site for the work as he has removed the old garage and has excavated the site for the footer. Lots of ledge. He will call when he has the forms in place.

Time 0.6

11-02-15	Permit 2015-49, 86 Columbus Jordan Road. Met with Lou to inspect the 			footer forms. He removed all the material (ledge) that he thought he 			couldn't get it all out. Forms okay and told him he could pour.

Time 0.6

11-09-15	Permit 2015-49, 86 Columbus Jordan Road. Lou called to have the foam 			block foundation forms inspected so he could pour. He tied it in neatly to 			the stone foundation and had rebar installed every row of blocks.

Time 0.3

11-20-15	Permit 2015-49, 86 Columbus Jordan Road. Inspected the garage footer 			forms with rebar. Told Lou the rebar needed to be supported.

Time 0.5

01-05-16	Permit 2015-49, 86 Columbus Jordan Road. I went by to see progress on 			addition. Most of the framing was completed except for the roof.

Time 0.9

03-08-16	Permit 2015-49, 86 Columbus Jordan Road. I went by to see the progress 			of the addition. All the manufactured beams and rafters were installed, 			roof sheathing installed, and the skylights. Sheathing installed on walls. 			Lots of support because of the cathedral ceilings using manufactured 			beams for some rafters.

Time 0.3

05-03-16	Permit 2015-49, 86 Columbus Jordan Road. Inspected the framing that has 		been completed. First and second floors of the addition and the second 			floor of the house. Lou needs to add a dormer on the side of the house to 			allow for a bathroom. The dormer will look like the one he is already 			constructed on the addition. He is getting ready to start the plumbing.

Time 0.5

07-20-16	Permit 2015-49, 86 Columbus Jordan Road. Lou called to have me inspect 		the holes for the rear deck, driveway side porch and backside porch. He 			wanted me to inspect some of the rough in plumbing and electrical so he 			could foam the outside walls. I told him he needed to fire stop holes 			between floors. He will be insulating the walls in the old section as well, 			walls not six inch but with the foam insulation it should be okay. All new 			wiring is being installed as all the walls are exposed.

Time 1.0

08-03-16	Permit 2015-49, 86 Columbus Jordan Road. Tony called to have me inspect the foam insulation. Both old and new addition was insulated. Looked okay.

Time 0.7

08-25-16	Permit 2015-49, 86 Columbus Jordan Road. Inspected the trench from the utility pole to the pedestal and to the addition with conduit and a base of sand. Okay to backfill.

Time 1.0

03-28-17	Permit 2015-49, 86 Columbus Jordan Road. Went by to see progress. Kitchen almost finished, bathrooms finished, flooring almost completed, and sheetrock installed. Still needs outside work including a deck for the second floor French doors from the bedroom.

Time 0.8

05-04-17	Permit 2015-49, 86 Columbus Jordan Road. Stopped by to tell Lou I sent a letter to owner saying permit expired and needs to be renewed. I did a quick inspection of the house and looked good, painters were almost finished painting all the rooms. I told Lou he needed to renew permit so I could issue a CO as all they needed to complete was the rear porch and the steps on the front of the house.

Time 0.3

03-22-17	Letter sent, no response, also notified Lou on 5/4, File to town hall.

07-14-17	Permit 2017-26. 86 Columbus Jordan Road. Lou called to have me do the final inspection of the new addition and the renovation of the existing house. Rear screened porch was completed as well a the small deck and steps on the front of the house. The only thing I found that needed to be done was a hand rail on the new stairs from the landing to the second floor. Lou will install railing and send me the picture so I can issue the CO.

Time 0.5

08-29-17	Permit 2017-26, 86 Columbus Jordan Road. Called Lou and left message about railing. He called today and sent me a picture of the railing. He thought he sent it earlier as he did the railing back in July. I will issue the Occupancy Permit.

David H Lersch

Plainfield Building Inspector