Shannon Smith

87 Underhill Road

542-1260

Permit #6037

Permit #2008-46

Permit #2009-34

Permit #2010-73

Permit #2011-48

Permit #2014-56

Permit #2015-48

Permit # 2017-53

07-14-06	87 Underhill Road, 6037. Contractor called wanting to know what was needed to get the permit approved. Told him what detail we needed and he will work with owner.

07-26-06	Telephone calls. Shannon Smith  6037, 87 Underhill Road as well as his contractor. Discussed inspections and the new set of plans Shannon gave the town. I was told that the building will be about four foot bigger.

08-09-06	Permit 6037, 87 Underhill Road. Inspected primary power installation and went over the buried utilities that will be installed with Jim the electrician and the general contractor. They will call when the conduit is laid prior to filling up the ditch.

Time 0:45

08-14-06	Permit 6037, 87 Underhill Road. Inspected footer forms with rebar installed on pedestals, wired together, and ground wire installed. Okay to pour.

Time 0:30

08-22-06	Permit 6037, 87 Underhill Road. Inspected wall forms. Very professionally done same as the footer forms. Rebar near the top and one row at the bottom. Told contractor it was okay to pour.

Time 0:20

06-27-07	On the way to another site  I stopped by 87 Underhill Road to see if there has been any activity since last fall. There wasn’t any. Permit 6037.

08-03-07	Permit 7067, 87 Underhill Road. Inspected 1500 gallon tank for solar heating and will also be used for a sprinkler system water supply. Trench from well and meter panel okay.

Time 0:20

06-16-09	Permit 2008-46, 87 Underhill Road. Steve said a lot of the structure was up so I went by to inspect. They are still working on the framing and insulation between posts and beams. There isn’t any electrical or plumbing started except for the panels that were installed before on the pedestal.

Time 0.6

09-17-11	Permit 2011-48, 87 Underhill. Shannon called to have me inspect the electrical panel and sub panel and the lower floor rough in electrical. We discussed his construction plans and asked about the wood stove chimney. It will be installed on the side of the single story section with the proper roof clearance, but had questions about the two story  portion of the structure’s roof will be above the top of the chimney but almost 20’ feet away. I told him to contract the fire chief to see if he had any ideas.

Time 0.9

05-05-16	Permit 2015-48, 87 Underhill Road. I inspected the radiant heat plumbing that was installed between the sub floor and the final wood flooring. I also inspected the hot water solar panels that were installed. They are not connected yet.

Time 0.8

05-20-16	Permit 2015-48, 87 Underhill Road. I met with Jim O. and Shawn to inspect the rough in electrical on the second floor. The wires are routed between the plywood and the final wood flooring that Shawn wants to install. The space between the floors contains the radiant heat pipes as well and the floors are separated by one inch wood strips.

Time 0.8

03-22-17	Letter sent, no response by 5/18-17, filed in town hall.

10-17-17	Permit 2017-53, 87 Underhill Road. Met with Shannon and inspected the new framing and the rough in plumbing for the kitchen and bathrooms. I also inspected the duct work for the forced air and A/C. I inspected the air handled to provide exhaust for the house and to bring in fresh air that will go through the heating/A/C system to heat or cool the incoming air. He has about two inches of spray foam in the rafters as well as fiberglass. For his main sewer pipe, he used four inch. He has radiant heat in the floors but with the thick wood floors he said he will need forced air heating as the wood provides too much insulation. Jim will start the rest of the electrical in December, after that the rest of the insulation will be installed.

Time 1.5

04-04-18	Permit 2017-53, 87 Underhill Road. Met with Shannon to inspect insulation in two areas, garage and other room that can be a garage or den.

He has been installing sheetrock in areas that have been inspected. Unless there are any changes or he needs advice the next inspection will be the final.

Time 0.7

.

David H Lersch

Plainfield Building Inspector