IRC 2018 APPENDIX Q

TINY HOUSES

Must comply to International Residential Codes, IECC, Life Safety Codes except for exceptions in Appendix Q

1.	Less than 400 square feet

2.	Ceiling height 6'8" minimum

3.	Bathroom / kitchen 6'4"

4.	Loft needs to be greater than 35 square feet, horizontal dimensions greater than 5'

Loft height less than 3 feet not counted in square footage.

5.	Stair width - above handrail greater than 17", below 20"

Risers 7" to 12"

Tread 20" - 4/3 riser		Riser 15" - 3/4 tread

example: tread 20 - 4/3 riser of 9" = 8"

example: riser 15" - 3/4 tread of 9" = 6.75"

Ceiling height, center of top riser 6'2" minimum

6.	Handrails refer to IRC 311.7.8

7.	Guards refer to IRC R312.1

8.	Ladders: rung wider than 12", 10"-14" rung spacing, support 200 pounds, 70-80 	degree from horizontal.

9.	Loft guards: greater than 36" or 1/2 height from loft to ceiling

10.	Bedroom egress: IRC R310.2

Loft bedroom egress window or skylight no more than 44" from loft floor IRC 	R310

Must meet foundation requirements for a home or (manufactured home?) requirements. (NH requires manufactured homes to be on at least a concrete slab.)