Matthew and Sarah George

PO Box 36

Meriden

359-1386

Permit # 2018-21

Map/Lot 102/14

Mud room/porch

113 Main Street

07-30-18	Permit 2018-21, 113 Main Street. I inspected the concrete tubes for the piers for the 11x9 mud room/porch.

Time 0.4

08-03-18	Permit 2018-21, 113 Main Street. Inspected the ledger board and additional work he did to repair some of the header. He had the manufactured beams installed on the piers. Looked okay.

Time 0.3

08-22-18	Permit 2018-21, 113 Main Street. Inspected the framing for the porch/mud room. Looked okay. Some of the existing deck was removed and the ledger board as the owner wanted to eliminate one of the two doors to the lower level under the deck and lots of rotten wood.

Time 0.5

09-06-18	Permit 2018-21, 113 Main Street. I inspected the insulation in the mud room, more than enough to meet code. Also inspected the moving of the downstairs door and the repair work to the header and new ledger for existing deck that was rotten. They are going to use barn wood in the mud room and wondered if they needed sheetrock first, I said yes unless the coat the wood with a fire retardant sealer.

Time 0.4

06-04-19	I inspected the completed mudroom and deck. Also the additional work on the lower door under existing deck and some repair of existing deck due to rot. I issued a Certificate of Completion.

Time 01.

David H Lersch

Plainfield Building Inspector