James and Elaine Lenz

PO Box 278

Meriden

469-3402

Permit # 2015-54

Map/Lot 102/15

House 62x28 with attached garage

115 Main Street

11-19-15	Permit 2015-54, 115 Main Street. I receive a call to inspect the footer forms for the new house. I told them about the rebar requirements and the ground wire. The panel will be in the garage so the ground wire will be in the garage footer. They had to go out and get rebar as they weren't going to put any in. Looked okay.

Time 0.4

11-24-15	Permit 2015-54, 115 Main Street. I received a call from the contractor last night asking about inspection of the perimeter drains. I said the inspection is required. I was concerned that the wall was already poured so I went out to look as I was going to Baynes Road for another inspection. he wall forms were almost ready but didn't have any rebar installed.

Time 0.4

11-24-15	Permit 2015-54, 115 Main Street. I received a call to inspect the wall forms and I said I was there earlier and he said they were installing the rebar and would be ready for inspection around noon. The rebar was installed and when I told them I like vertical rebar installed in the footer, four feet apart and that the small V in the footer to stop the wall from moving wasn't enough. He said he couldn't find out what the town required on our web site about rebar. May be a good idea to add requirements for foundations on the web site. I told them they could pour.

Time 0.5

11-30-15	Permit 2015-54, 115 Main Street. Inspected the footer forms with rebar installed and supported on chairs. Looked okay.

Time 0.5

12-01-15	Permit 2015-54, 115 Main Street. I inspected the frost wall forms for the attached garage. Two rows of rebar installed. Vertical rebar was installed in the footer. Looked okay.

Time 0.6

12-21-15	Permit 2015-54, 115 Main Street. Went by to look over construction. Garage floor was poured and the basement floor had three inches around the inside perimeter and over the stone. Looked okay.

Time 0.1

06-14-16	Permit 2015-54, 115 Main Street. The modular house was set on the foundation. Did a walk through and around perimeter.

Time 0.4

07-14-16	Permit 2015-54, 115 Main Street. Stopped in to see progress. Porch and rear decks being constructed. Looked okay.

Time 0.2

07-20-16	Permit 2015-54, 115 Main Street. The electrician called to have me inspect the service entrance, meter panel installed on right side of garage entrance and cables to eve, keeping over three feet away from door on second floor. Aerial service and new poles already in place.

Time 0.7

07-20-16	Permit 2015-54, 115 Main Street. Notified Liberty Utilities via email that it is ready for service.

Time 0.1

08-22-16	Permit 2015-54, 115 Main Street. I inspected the upstairs over the garage for the rough in electrical and the second floor insulation. Cabinets installed in kitchen and bathrooms.

Time 0.5

10-04-16	Permit 2015-54, 115 Main Street. House getting close to completion. Electrician installing generator and transfer switch. Wire for dish washer comes out of the wall behind where the washer goes, needs to move to cabinet with receptacle, also wires for microwave need to be moved in cabinet above for receptacle. Wiring done by modular company for those errors. Should be all completed by end of month.

Time 0.6

10-19-16	Permit 2015-54, 115 Main Street. Met with solar contractor and inspected the roof mounted solar panels with micro inverters. Labels were installed on the meter panel, the outside disconnect switch, the main circuit panel and breaker for the solar system, and the small solar panel with a 20 ampere breaker for each section of the three solar panels. I also inspected some of the plumbing in the basement and the installation of the propane standby generator.

Time 0.7

10-27-16	Permit 2015-54, 114 Main Street. Stopped by as they are nearing completion. Tested out generator operation. The solar AC is fed to the three 20 ampere circuit panel, then to the 50 ampere disconnect breaker outside then to the utility side of the generator transfer switch, according to the electrician. The wire for the dishwasher goes to a junction box, then to a receptacle in the sink cabinet. The appliances should be here tomorrow and other than railings, painting they should be ready next week for a final.

Time 0.9

11-03-16	Permit 2015-54, 115 Main Street. I stopped by before heading out of town as they thought they would be ready today. Still not completed. Appliances in, laundry area not completed, stair railing needs to be installed. Still finishing sheetrock and painting.

Time 0.6

Jim / Elaine Lenz – 115 Main Street   New Home – Final C.O.

Date: Nov, 2016         Permit #:2015-54          Activity: Final inspection for C.O. Met builder and owner on-site. Interior railings installed at balcony and stairs. No exterior railings on “Front” porch (east). Grade at deck perimeter <30” all sides. Grade at 5’ from deck edge >30” in some areas. Should be corrected. Electrical access below panel in wall between garage and house needs to be sealed. Discussed options w/ owner. Owner to speak to builder re: sealing wall. Due to recent snowfall owner opts for temp C.O. and will correct grade off porch in spring.

25 min. Brad

12-13-16	Permit 2015-54, 115 Main Street. Brad said hole closed and due to snow they may have to wait until spring for the landscaping. I will issue the Occupancy Permit.

David H Lersch

Plainfield Building Inspector