Marianna McKim

94 Bonner Road

469-3999

Permit # 2018-73

Map/Lot 105/10

24X24 LAVALLEYS GARAGE

06-05-19	Received response back from Marianna that they haven't started yet.

10-16-19	Charlie called and said the slab was ready for inspection, when I got there it was poured and forms off. I let them know I needed to see prior to pouring, not after.

Time 0.5

11-25-19	I inspected the garage while I was there to inspect the solar installation. It was almost completed except siding and electrical.

Time 0.2

12-31-19	Receiving emails about status, permit not renewed yet but Brad waiting for okay to do final.

1/13/20     94 Bonner: Sonnenberg - Garage Final

Met Owner on-site and walked through the new building. Sill anchor bolts visible, spaced ok and connected. Panelized walls. Stairwell w/handrail. Trussed roof system braced and blocked. Exterior finish complete. Grading away from building ok. Power panel labeled.

Everything looked good, complete. I indicated to owner that Dave would issue the C.C.

01-30-20	Brad did final and waiting for his report. I will issue a certificate of completion based on his verbal report.

David H Lersch

Plainfield Building Inspector

Completion Certificate

TOWN OF PLAINFIELD, NH

This certifies that the work described by Building Permit # 2018-73, at 94 Bonner Road, Meriden, NH, Map/Lot 105-10 has been completed in accordance with the provisions of the International Residential 2015 Code and the Codes of the Town of Plainfield.

Description of Work: A 24'x24' two car garage on a concrete slab with electrical service.

Portion of structure inspected: Completed garage

Applicants Name: Reinhart Sonnenburg

94 Bonner Road

Meriden, NH 03770

January 30, 2020

Building Code Official Signature   Date										        David H. Lersch