Kimball Union Academy

PO Box 188

Meriden

469-2152

Permit # 2018-80

Map/Lot 105/31

KUA Ops. Facility

Behind 37 Main Street

12-07-18	Permit 2018-80, KUA Ops facility behind 37 Main. Wall pre-pour: met 			Doug / Osgood rep on-site wall formwork still in progress. Planning to 			pour in 2 sections for better mixer access to walls. Cold joints keyed. 			Horiz. Rebar passes through keyed joint. Other rebar /anchor steel appears 		per drawings. OK to pour.  BRAD

02-06-19	Permit 2018-80,KUA Ops facility behind  37 Main

Email/phone follow-up with DES/KUA after KUA discussed intent for 			floor drains/collection tank (but no plans/description/permit on file). 			Verified need for system approved by DES. Doug agreed to keep us in the 			loop. He understands that we will need to see approved design docs and 			inspect system.

02-08-19	Permit 2018-80, KUA Ops facility behind  37 Main

Reviewed pics of KUA Ops Facility sub-slab vapor barrier

02-12-19	Permit 2018-80, KUA: Ops facility behind 37 Main.

Slab pre-pour inspection.

Met crew lead on-site for pre-pour inspection (1st Half of ground 			floor slab). Work complete. Vapor barrier, Insulation, Radiant 			tubing, rebar in place. Everything looked neat/complete. Gave 			Osgood Constr. Ok to pour. Texted Doug.  Emails,  Doug, you,  re: 			power / Liberty

02-12-19	Permit 2018-80, KUA Ops Facility behind 37 Main.

From: Doug Plummer <dplummer@kua.org> 
Sent: Tuesday, February 12, 2019 10:45 AM
To: aci.builds@comcast.net
Subject: FW: KUA

Hi Brad,

Thank you for getting in early and approving the pour this morning.  That section is all poured and looks great!

I believe that they plan to pour the mezzanine on Thursday so if you could stop by tomorrow afternoon that would be great.

While you’re here, the next trip, can you please do whatever is needed to do an inspection that would allow Liberty Utilities to get in and get the power in?  I thought that you’d approved the panel location so I don’t know what else they need … I’m hoping that you do.  (Please see below.)

Thank you very much!

Doug

02-12-19	Permit 2018-80, KUA Ops Facility behind 37 Main.

Hi Dave,

Here is the thread from Doug. I have inspected the temp power set-up (Board mounted meter socket & disconnect) and It is ok. According to Doug Liberty has set the transformer and is ready to set the meter, but needed the ok called in.

Let me know if there is anything further you want me to do.

Regards,

Brad

02-12-19	Permit 2018-80, KUA Ops Facility behind 37 Main.

New service for Kimball Union Academy Operations Center, Meriden, NH has been

inspected and it is okay to connect to utility. WO # 301838-01008

02-13-19	Permit 2018-80, KUA Ops facility behind 37 Main.

Mezzanine slab on deck pre-pour inspection..

Coordinated w/Doug for pre pour inspection (Doug couldn’t be there). 			Deck, curbing, rebar in place. Everything looked good. Contacted Doug 			w/Ok to pour.

02-25-19	Permit 2018-80, KUA Ops facility behind  37 Main.

Slab pre-pour inspection.

Met crew lead on-site for pre-pour inspection ( 2nd Half of ground floor 			slab). Work complete. Vapor barrier, insulation, Radiant tubing, rebar in 			place. Everything looked neat/complete. Gave Osgood Constr. Ok to pour. 		Texted Doug.

03-15-19	Permit 2018-80, KUA Ops Facility. Rough-in (partial offices /laundry 		etc.). Walked through all rooms w/Lead Electrician then again 			w/Lead plumber. Everything coming together (still wrapping up). 			Everything plated. Vents not run through roof yet, but area above 			ceiling will be visible/accessible. Ok to hang drywall in those areas.

03-18-19	Permit 2018-80, KUA Ops Facility

Hi Dave,

Last week I was called to the new KUA Ops Facility for pre-drywall electrical/plumbing rough-in inspection. I the course of that inspection I asked about the status of the floor drain system. The last I had heard was that they understood they would need to satisfy NH DES regs, which require a design, application, and permit. KUA had agreed to keep us in the loop. I have heard nothing from them about this since then. As I was inspecting the plumbing they showed me where the tank ports were protruding from the back/west drive area. The tank is in and buried, controls/alarms pending. I told the site supervisor that, as with any part of the project construction, we should have been called to see it before it was back filled. Iâ€™m not sure whether DES cares as long as they have an applicant on the hook (via the permit process) in the event ofÂ  a problem in the future.

This morning Doug responded with the message below, and you can see my response. In retrospect I think I should have spoken to you before responding. I hope you are ok with my response. Let me know if you want me to do anything further.

I have called Steve on this because I think there is a policy issue involved here: I think we should be more consistent in requiring that design docs for permits be submitted before work is started / covered, and that perhaps there should be consequences when that does not occur. KUA is probably the most capable of complying with the normal (design-review-approve-construct-inspect) process, but, at least in my experience, the most frequent offender.

Regards,

Brad

To: Doug Plummer <dplummer@kua.org>
Cc:

Hi Doug,

For the drain collection system the Town's official interest is that the State regs are satisfied, and to be aware of the existence of hazardous materials and their control systems. So I'm surprised that DES would be OK with that sequence. However if they are ok DES we will be ok and I'll look forward to seeing the design docs.

In general we should see design docs before work begins. As I have indicated to you before, I would like to work with KUA to make that happen on every KUA project.

Regards,

Brad

On Mar 18, 2019 7:38 AM, Doug Plummer <dplummer@kua.org> wrote:

Good Morning Brad,

I got your message last week but have been straight out and didn't have a chance to reply.

As soon as they get the tank monitoring equipment installed, and we get power to it, I will get an as-built drawing to you and the state so that we can register the tank. Does that work for you?

Thank you,

Doug

03-20-19	Permit 2018-80, KUA Ops facility. Rough-in (partial): Walk-through 			areas not covered in previous inspection. Everything straight 			forward except outlets in 1hr wall between areas that will eventually 		have a metal wall covering. Agreed with electrician to fire-caulk 			around all device boxes / extensions to maintain fire/smoke 				separation. Same procedure will be followed around flush mount 			radiant floor manifold enclosure. One partition remaining to be built. 		Otherwise ok to drywall inspected areas.

05-07-19	Did a walk through with Brad and Doug Plummer. Separation between 			garage and offices was not sealed, just insulation. Some receptacles in 			garage area in fire wall not fire stopped.

Time 0.4

05-08-19	EMAIL FROM DOUG PLUMMER

The guy from Osgood tells me that he will make sure that he takes care of the air leaks between the front and back of the building.  I’ll let you know when that has been completed.

Douglas R. Plummer

Director of Facilities and Operations

06-11-19		Did a walk through to see progress. Fire stopping was taken care of as

well as the open separation between office area and rear of building

shop area. Boiler installed and piping, some bath fixtures need to be

installed.

Time 0.5

07-30-19		Inspected the facility and other than some handicap rails in bathrooms

and floor trim and other small items it is okay to be occupied and I

will send a note to Doug that it okay to use and will issue the CO next

week when small items are completed.

Time 0.4

08-22-19	I completed the final inspection of the Ops Center. Bathrooms finished, egress door in hallway had an egress sign but no panic bar on last visit, it was now installed. I will issue a Certificate of Occupancy.

Time 0.6

David H Lersch

Plainfield Building Inspector