DATE:  06 / 13 /2019

Permit Status (Valid for one year from issue date)

Permit # ___2018-40_______  issued:  _07_/ 11 / 2018

__X__	RENEWAL REQUIRED BY ___07_____/___10__/__2018__

____	EXPIRED,  NO INSPECTION REQUESTED

_X___	LAST INSPECTION:   10 /30 /2018

_X___ 	YOUR PERMIT REQUIRED INSPECTIONS PER  INSPECTION 				GUIDELINES (SEE INSPECTION GUIDELINES ATTACHED)

____	CLOSED  – YOUR PERMIT IS CLOSED, A NEW PERMIT IS REQUIRED

____	A CERTFICATE OF OCCUPANCY WAS REQUIRED PRIOR TO OCCUPYIING YOUR HOUSE

__X__	A CERTICICATE OF COMPLETION WAS  REQUIRED

NAME       Plainfield Community Baptist Church

ADDRESS  PO Box 84

Plainfield, NH 03781

MAP/LOT __107-6___ ADDRESS 1094 Route 12A Parsonage

Plainfield Community Baptist Church

1094 Route 12A

Permit # 2017-24

Permit # 2018-40

Map/Lot 107/6

Parsonage

adding wall to make office and electrical

10-13-17	Permit 2017-24, 1094 Route 12A. John called and wanted me to inspect the rough in electrical wiring he installed in the room that is now two rooms, one a new office. Added 2x4 along outside wall as there was only wood, no insulation. He installed some in the new wall. Looked okay.

Time 0.4

05-29-18	Permit 2017-24, 1094 Route 12A. No additional inspections requested. 			Sent status letter.

06-02-18	Permit 2017-24, 1094 Route 12A. Stopped at flower sale in town. They 			were working inside. I let them know permit expired and it was only to 			make an office. All the walls were stripped. They were building stud walls 		against the outside walls. Also a large beam was cut as the original 				chimney was there. They built walls to make office and a living room 			space helping support the joists that the beam was supposed to do. They 			also found live nob and tube electric wires that they were going to remove. 		Shoring up walls, wiring, and additional insulation is what they are doing. 			They will be getting a permit (renew and adding scope).

Time 0.3

07-26-18	Permit 2018-40, 1094 Route 12A. They wanted me to stop by as they had 			some questions. We went over placement of detectors. One smoke in each 			of the bedrooms (4), smoke/co outside three bedrooms in upstairs hall, 			smoke/co in room outside master bedroom, smoke on first floor and 			smoke/co in basement. They are making large room in to two bedrooms 			upstairs and creating closets. Areas that I inspected already had new 			insulation installed, built new 2x6 framing to existing outside walls. Okay 			to continue.

Time 0.4

08-01-18	Permit 2018-40, 1094 Route 12A. Inspected some more rough in electrical and placement of detectors. I let them know that they could insulate.

Time 0.6

Hi DAVE

08-31-18	Permit 2018-40, 1094 Route 12A. Parsonage – electrical rough-in 			(second floor only) – Met Marc Overman on-site, my first visit to 			project. He walked me through the second floor renovations and I 			check the electrical rough-in. Detector feeds where they should be 			and Marc said they are interconnected. Lighting circuits for 				bedrooms/closets as needed. Outlet layout sub-panel location 			looked ok. I told then they were ok to insulate.

I returned on Saturday. The insulation was 99% complete. 				Everything looked neat/tight except a couple of gaps which Marc 			said they would address. I told them they were ok to sheetrock.

Brad

09-19-18	Permit 2018-40, 1094 Route 12A. Inspected downstairs hallway for 			rough in electrical so they could install sheetrock.

Time 0.3

10-09-18	Permit 2018-40, 1094 Route 12A. Marc called about the codes for the front steps they want to change. He didn't leave number, just message. Went by today to look at what was there. Three foot door with side light panels. I left message that four to five feet would be okay, that would give from six inches to one foot on either side of the entrance.

Time 0.3

10-30-18	Permit 2018-40, 1094 Route 12A. Met with Marc to go over work that has been completed as they need to have pastor move in soon. Carpet being laid. Walls being painted. Need to replace receptacles with child proof ones, not a stopper for moving in but needs to be done before Occupancy Permit. Heating pipe going from basement to second floor needs fire stopped. Other than that I didn't see any other codes issues.

Time 0.7

09-08-19	Renewal letter sent in June, No response as of this date. Expired without a final inspection.

David H Lersch

Plainfield Building Inspector