Dennis and Corinne Girouard

1145 Route 12A

675-2471

Permit # 2015-09

Permit # 2016-20

Permit 2017-73

Permit 2018-85

Map/Lot 108/28

windows, siding, basement to separate apartment

added sun room to permit

11-23-15	Permit 2015-09, 1145 Route 12A. Dennis called and wanted my to come by and go over his plans for the apartment. The siding and windows are installed. No issues with egress windows. He is just getting ready to do some framing and has added an additional 2x8 to the existing 2x8 floor joists. We discussed heating as he will be installing hot water heating.

Dennis will keep me in the loop.

Time 0.7

03-09-16	Permit 2015-09, 1145 Route 12A. Dennis called to have me inspect his wiring for the apartment. Looked okay except had some low voltage wiring close as well as in the same as 120VAC wiring. I told him he couldn't have low voltage in same holes and should be about four inches away. He will reroute the central vacuum, thermostat wiring, and phone and network wiring. We discussed his upcoming permit for an addition as well as current insulation codes.

Time 0.9

03-22-16	Permit 2015-09, 1145 Route 12A. Met with Dennis and inspected the insulation he installed. Everything looked okay.

Time 0.5

07-01-16	Permit 2016-20, 1145 Route 12A. Inspected the wall forms with the rebar installed. Saw pictures of footer that was poured when I was out of town. Okay to pour.

Time 0.3

07-14-16	Permit 2016-20, 1145 Route 12A. Inspected the floor forms with rebar installed. Looked great, plenty of support.

Time 0.3

10-31-16	Permit 2016-20, 1145 Route 12A. Met with Dennis to inspect the insulation in his sun room. It stays warm in there even without heat. Well insulated. Will do the final in the spring.

Time 0.4

06-04-19	Did the final inspection of the sun room the basement apartment. two bedrooms, one office or den, kitchen-living room, and bathroom. CO/smoke in living room outside bedrooms and smoke in the three other rooms. Dennis needs to install child proof receptacles and arc fault breakers for a few circuits. Windows in the two rooms, need to verify size, looked okay but did not measure. I will issue a six month temporary so his son can move in while he changes breakers and receptacles.

Time 0.8

10-08-19	Inspected the new sub-panel that he used for the new circuits with the arc-fault breakers installed as well as inspected the child proof receptacles that were installed. I will issue a Certificate of Completion.

Time 0.6

David H Lersch

Plainfield Building Inspector