Ryan & Emily Boynton

PO Box 212

Meriden

510-0025

Permit # 2015-46

Map/Lot 102/2

dormer and entryway

102 Main Street

11-03-15	Permit 2015-46, 102 Main Street. Received a call to inspect the framing of 		the dormer. Framing looked okay but the new four windows, two in the 			bathroom and two in the bedroom are the same size and although they are 			okay for the bathroom the don't meet egress for the bedroom.

I gave the home owner some suggestions and the contractor called and he 			said he wanted to keep the dormer windows the same size and besides the 			dormer has all the siding on already. I told him that is why I like to be 			contacted prior to starting so we don't have these issues. The contractor 			should have known about egress windows and it has been code for years.

They were going to put a small window on the rear end of the dormer. I 			gave him the egress codes, 5.7 sq.ft. 44 inches from floor. I don't know if 			he can get the correct size in the space and meet the 44 inch requirement. 			He said he could build a platform under the window and I told him that 			that would not be a good solution but could be made to work.

Time 0.5

12-21-15	Permit 2015-46, 102 Main Street. No one home but they did install an egress window in the bedroom and the new entry way (porch) was completed and the front edge was supported on concrete piers.

Time 0.1

07-11-16	Permit 2015-46, 102 Main Street. Inspected the rough in plumbing and electrical for the dormer. Looked okay, will call when insulation is installed.

Time 0.4

06-30-17	Permit 2015-46, 102 Main Street. Letter sent 3/17/17, no response as of 6/30/17. Closed without CO.

David H Lersch

Plainfield Building Inspector