Alan & Myra Ferguson

109 Jenny Road

469-3399

Permit # 2013-33

Map/ID #  215/21

Modify porch to extend kitchen and modify roof for HW solar

07-19-13	Permit 2013-33, 109 Jenny Road. Myra called to have me inspect the work that was being done. A section of the porch was removed and they were framing the addition to the kitchen. The footer and frost wall were already poured and backfilled. Alan showed me pictures of both and looked okay. They will be putting radiant heat in the kitchen addition and I told them I needed to see it with pressure before it is covered over. I let Alan know that I should have been called for the concrete work and since a lot of the work was completed prior to requesting a permit, they didn’t have the inspection sheet.

Time 0.3

08-28-13	Permit 2013-33, 109 Jenny Road. I went to inspect the rough in electrical wiring, radiant heat plumbing, and the installation of addition solar panels. Looked good. They will be spraying foam insulation and coating attic and crawl spaces with a fire retardant. The solar is almost completed and I will inspect it on Tuesday as well as the insulation.

Time 1.0

09-03-13	Permit 2013-33, 109 Jenny Road. I inspected the sprayed foam insulation and told them they could cover walls, etc. and I did the inspection of the completed addition to their electrical solar system.

Time 0.6

David H Lersch

Plainfield Building Inspector