Alan & Myra Ferguson

109 Jenny Road

469-3399

Permit # 2014-30

Map/ID #  215/21

Two 3’ bump outs & 10x16 addition to bedroom

06-09-14	Permit 2014-30, 109 Jenny Road. Inspected the forms, rebar, and insulation of the three additions to the-guest house. This was for the enlarging the bathroom and kitchen, and a new bedroom. The sections of the floor that will be at ground level will have blue foam on the outside edge of the floor to below frost line.

Time 0.5

06-11-14	Permit 2014-30, 109 Jenny Road. I did the Inspection of the drain plumbing that will be under the slab and was pressurized. Looked okay and pressure holding.

Time 0.7

06-20-14	Permit 2014-14, 109 Jenny Road. I inspected the blue foam around the slabs for the additions.

Time 0.1

07-14-14	Permit 2014-14, 109 Jenny Road. Went to inspect the rough in electrical wiring. Looked okay and they are going to spray foam insulation.

Time 0.4

David H Lersch

Plainfield Building Inspector