Matthew & Emily Marrazzo

1457 N Hemlock Road, Charlestown 03603

359-7782

Permit # 2013-08

Map/Lot 212/23 & 213/23 ?

40x28 2 story sfh w/attached 26x26 two car garage

111 Croydon Turnpike

04-23-13	Permit 2013-08, 111 Croydon Turnpike. I received a telephone call yesterday to see if I could go by and inspect the footer forms. I did the footer inspection for the house. Looked okay and told them they could pour.

Time 0.4

04-29-13	Permit 2013-08, 111 Croydon Turnpike. I inspected the wall forms for the

house. Looked okay and gave the okay to pour. The garage work will be

completed after the walls are poured and the basement floor as well as the

perimeter drains and backfill.

Time 0.3

05-01-13	Permit 2013-08, 111 Croydon Turnpike. Contractor called to have me inspect the temporary electrical service. Meter socket and breaker panel mounted on plywood post and secured with three braces. It was okay and notified Liberty.

Time 0.4

05-03-13	Permit 2013-08, 111 Croydon Turnpike. I inspected the perimeter drains, foundation coating and drain plumbing that will be under the basement floor so they could do the radiant heating pipes.

Time 0.7

05-07-13	Permit 2013-08, 111 Croydon Turnpike. I inspected the floor insulation, vapor barrier and the pressure tested radiant heat piping. I told them they could pout the concrete floor.

Time 0.9

07-08-13	Permit 2013-08, 111 Croydon Turnpike. I inspected the rough in plumbing and electrical as well as the framing. Everything looked okay and they were planning on spraying the foam insulation today.

Time 0.9

07-09-13	Permit 2013-08, 111 Croydon Turnpike. I inspected the sprayed foam insulation. Looked okay.

Time 0.7

07-29-13	Permit 2013-08, 111 Croydon Turnpike. I inspected the electrical trench with conduit installed from the pole to the house and from the house to the generator pad. I told them they could backfill.

Time 0.3

08-06-13	Permit 2013-08, 111 Croydon Turnpike. I inspected the service entrance wires from the pole to the house, meter panel with disconnect, generator transfer switch, and the mail circuit panel. Looked okay and notified power company, work order 14559734.

Time 1.0

David H Lersch

Plainfield Building Inspector