Richard and Elizabeth Morse

1116 Stage Road

709-7144

Permit # None

Map/Lot 240/20

Install a Vedolux 55 Boiler using a Viking Bio 35 pellet burner, 170,000BTU/hr. when using pellets. The system has a 4 ton pellet hopper and feeds the boiler. The hot water from the boiler keeps hot water in storage tanks that are connected to the  roof mounted hot water solar panels. The storage hot water is distributed to either radiators or to a forced hot air heat exchanger.

02-09-16	Permit - Never applied for one. Owner wanted to have pellet boiler inspected and Frank (Fire Chief) called me and we set up a time to go over. When we arrived, we found a solar hot water unit on the roof and the rest of the system was in the basement. The system consisted of a large pellet bin for auto feeding the pellet boiler. The boiler supplied hot water to a heat exchanger mounted in the ductwork of their forced air furnace. It also provided hot water to storage units that were part of the roof mounted solar hot water system. It was installed correctly but he needs to have a CO detector mounted in the basement, connected to the rest of the monitored fire alarm system. When he gets that installed I will issue a Completion Certificate so he can get energy credit.

Time 0.9

03-31-16	Permit - none (was advised by Town Hall that a permit wasn't required, it 			is too late for one now). Richard called me to inspect the installation of the

CO detectors that the Fire Chief required. I inspected the installation of the

detectors. A plug in detector was installed in the second floor hallway 			outside the bedrooms. Two more were installed (battery only), One at the 			top of the main stairs that went to the boiler location in the basement, the 			other one battery only) was mounted at the top of the second set of 				basement steps that came down behind the boiler location. I will issue a 			Completion Certificate.

Time 0.5

David H Lersch

Plainfield Building Inspector