Julie Murray

118 Kenyon Road

675-6178

Permit # 7024

Map/Lot 261/17

07-19-07	Permit 7024, 118 Kenyon Road. Stopped by to talk to owner as I noticed a trench dug from the pole and also because of the PSNH site requesting changing from aerial to buried service. Contractor was there and I went over inspections.

Time 0:25

08-06-07	Permit 7024, 118 Kenyon Road. Inspected the footer forms for the addition. Looked okay. Told them they could pour.

Time 0:35

08-07-07	Permit 7024, 118 Kenyon Road. Inspected the frost wall forms for the addition. Okay, told them they could pour.

Time 0:25

08-31-07	Telephone calls while out of town.

Got a call from Thresher Electric regarding getting PSNH out to connect electrical power. I was never called to inspect the trench with the conduit installed and prior to covering. This was covered on one of my earlier visits with owner and contractor. Not sure what action I will take prior to letting PSNH know it is okay to run cables and connect.