Abigail Harrington

1491 Route 12A

359-0090

Permit # 2018-14

Map/Lot 258/4

ground mounted solar

05-14-18	Permit 2018-14, 1491 Route 12A. I inspected the ground mounted solar array and the trenches with conduit installed to the house, the shed, and the tree house. Looked okay and told them they could backfill.

Time 0.7

05-17-18	Permit 2018-14, 1491 Route 12A. Jim O. called and said they were ready for the solar inspection. Inspected the solar panel on the house as it uses micro-inverters and AC comes from the solar array. Inspected panel in shed and house for disconnects and labels. I received an email with COC for Eversource to sign, signed, scanned and emailed back to solar company. Jim still has to connect circuits to shed panel, wiring to tree house and from shed to chicken coop. He will call when all wiring is completed.

Time 0.9

05-22-18	Permit 2018-14, 1491 Route 12A. Jim called and said wiring was finished. Inspected wiring and panel in shed, wiring to chicken coop, wiring to tree house. All looked okay. Tree house on a double GFI breaker. I will issue a Certificate of Completion.

Time 0.7

David H Lersch

Plainfield Building Inspector