Michelle Martino

15 Ladieu Road

469-3001

Permit # 2010-70

Map/Lot 234/19

Removal of old greenhouse and make a new room

11-24-10	Permit 2010-70, 15 Ladieu Road. I met with the contractor to inspect the radiant heat piping in the greenhouse so they could pour the concrete floor. It was okay. There will be some new electrical wiring and the metal/glass greenroom will be removed and replaced with a small addition.

Time 0.5

01-03-11	Permit 2010-70, 15 Ladieu Road. I received a call from the contractor to inspect the rough in electrical. I called Win and he said he would handle and email me the results.

Dave, 01-06 I went and did an inspection at 15 Ladieu Road. There has been constructed a room to replace the attached metal frame green house. The electrical work consists of 2 GFCI protected outlets and provisions for an overhead light with a paddle fan . The rough in electrical work was okay. The contractor wanted to get approval to insulate and sheetrock. The framing looked good, so I gave him the okay to proceed knowing that you might not be back for a few weeks. Win Spencer

David H Lersch

Plainfield Building Inspector