Siegfried Hoermann

621 Pleasant Street

PH#

Permit # 2011-50

Map/ID # 254/12

SFH w/attached garage at 176 Center of Town Road

11-15-11	Permit 2011-50, 176 Center of Town Road. I was called to inspect the footer forms for the house. The forms were okay with rebar installed correctly and ground wire attached. Gave okay to pour.

Time 0.7

11-18-11	Permit 2011-50, 176 Center of Town Road. I was scheduled to inspect the trench with conduit at 10AM. I went there and the conduit was installed from the last pole on the driveway almost to the frost wall forms. Sand was installed, at least six inches below the conduit and would be covered with at least the same amount. The frost wall forms were almost ready to pour with rebar installed so I told them they could pour. The rest of the conduit will be installed when the wall forms are removed.

Time 0.3

11-21-11	Permit 2011-50, 176 Center of Town Road. I inspected the footer forms for the garage. Looked okay, told them they could pour.

Time 0.4

12-01-11	Permit 2011-50, 176 Center of Town Road. Inspected the plumbing that will be below the concrete slab. I also inspected the frost wall forms for the garage.

Time 0.4

02-09-12	Permit 2011-50, 176 Center of Town Road. I inspected the meter panel and the temporary circuit panel so NH Co-Op could pull the cables from the pole through the buried conduit to the meter panel.

I notified NH Co-Op that it was okay.

Time 0.4

03-27-12	Permit 2011-50, 176 Center of Town Road. I inspected the radiant heating pipes over blue foam so they could pour the concrete floor. Looked okay.

Time 0.5

04-19-12	Permit 2011-50, 176 Center of Town Road. I inspected the rough in electrical wiring and the plumbing. The electrical was ready to have the walls closed up but some of the plumbing wasn’t completed yet. I also told the plumber that I wanted the drains and water lines presser tested and when they were ready to call. I let them know that they could insulate the outside walls. That should be completed for me to inspect around Wednesday next week so they can install sheetrock. In the spare bedroom neither of the two windows qualify for egress and one of them will have to be changed.

Time 0.6

04-24-12	Permit 2011-50, 176 Center of Town Road. I inspected the rough in plumbing that was completed and pressurized. The insulation wasn’t there yet and the spare bedroom window is on order.

Time 0.6

05-09-12	Permit 2011-50, 176 Center of Town Road. I inspected the blown insulation in the walls. Looked okay. They will close in the outside walls.

Time 0.5

David H Lersch

Plainfield Building Inspector