Pete and Emily Twarog

PO Box 407

Meriden

802-280-8013

Permit # 2016-11

Map/Lot 233/26

30x24 addition

178 Chellis Road

05-10-16	Permit 2016-11, 178 Chellis Road. I inspected the footer forms for the addition. There was some water but a drainage trench was being dug and drain pipe installed and backfilled as they went. This will be for the perimeter drains. The concrete contractor Dave said the had to pump out the water to do the forms, but since the pipes are installed the water is draining.

Time 0.4

06-07-16	Permit 2016-11, 178 Chellis Road. I inspected the wall forms with rebar installed. Looked okay.

Time 0.7

06-14-16	Permit 2016-11, 178 Chellis Road. I inspected the new buried electrical service and notified Liberty Utilities.

Time 0.5

07-11-16	Permit 2016-11, 178 Chellis Road. Peet called to let me know the new meter panel was installed on the house and that the cables were pulled and a coil at the pole with 10' of metal conduit. Work order 146996-147008 for Liberty Utilities.

Time 0.7

07-22-16	Permit 2016-11, 178 Chellis Road. Peet called to have me do a rough in electrical and plumbing inspection. Everything looked okay. Told them to call when insulation is ready for inspection.

Time 0.7

09-09-16	Permit 2016-11, 178 Chellis Road. Peet called to have do a walk through to see what items needed to be completed for a CO. The water heater and the oil fired boiler needed relief valve plumbed to 4" from floor. I asked him if he filled out Oil permit for the state, said no, told him to go to town hall, fill out and get with Frank. Other than some minor construction items that were being worked on, it is almost ready.

Time 0.7

10-17-16	Permit 2016-11, 178 Chellis Road. Met with Peet to do the final inspection 		of the addition. Frank inspected the new oil boiler. I inspected the new 			water heater, boiler and associated plumbing. I also inspected the electrical

and the new bathroom. The new bedrooms that replaced the two in the old part of the house had egress windows and all the smoke detecters were installed and tied to existing detectors. I will Issue an Occupancy Permit.

Time 0.6

10-17-16	Permit 2016-11, 178 Chellis Road. Created and printed Certificate of Occupancy.

Time 0.3

David H Lersch

Plainfield Building Inspector