Lee & Betsy Lynd

181 Bean Road

469-3379

Permit # 2012-54

Map/Lot 250/4

8’ addition to east side of house

10-12-12	Permit 2012-54, 181 Bean Road. Bill called to have me inspect the footer forms for the addition. Looked okay and let Bill know it was okay to pour. They will be using foam blocks for the foundation walls.

Time 0.8

11-29-12	Permit 2012-54, 181 Bean Road. Bill called to have me do the rough in inspections. They had to replace a lot of the electrical wiring in the two rooms that were having the addition put on due to rodent chewing. An egress window in the bedroom upstairs that is being enlarged was installed and some plumbing and electrical work in the upstairs bathroom. Bill had a new smoke detector in the upstairs hallway and in the new bedroom. I suggested that they may want to install one in the bedroom that wasn’t being worked on and that the one in the hall should be a combination CO/Smoke detector. Bill said he would install the CO/smoke in the hall and approach the owner to use the removed smoke in the bedroom. They were insulating the whole outside of the house with two-inch foam insulation.

Time 0.5

David H Lersch

Plainfield Building Inspector