Philip G Hallam, Rev Trust

PO Box 310

Meriden

469-3593

Permit # 2016-03

Map/Lot 101/8

Renovations

22 Colby Hill Road

01-25-16	Permit 2016-03, 22 Colby Road. The owner called to have me look over the renovations. The current stairs to the second floor doesn't have the required head room do to the roof as it is more of a story and a half and the stars are on an outside wall. They want to widen the stairs to the right to give more headroom. Other than moving the stairs or changing the roof this sounds like a good solution. New vinyl window inserts were installed and are only a shade less than 5.0 square feet instead of the required 5.7 square feet. Since they are only inserts they can stay.

Time 0.9

02-05-16	Permit 2016-03, 22 Colby Hill Road. I completed the rough in electrical and plumbing inspection. Okay to insulate.

Time 0.7

02-13-16	Permit 2016-03, 22 Colby Hill Road. I did the sprayed foam insulation inspection and looked okay.

Time 0.9

03-31-17	Permit 2016-03, 22 Colby Hill Road. Received a call to inspect the rough in electrical and plumbing on the space above the garage. Looked okay. Garage ceiling will have to have sheetrock as well as the wall that against the house. I told Phillip I could issue a CO for the house renovations as I looked at the completed renovations for the main house which what the permit was for and he could apply for a permit to do the garage or he could renew the permit as it has expired and add the garage work to the original permit..

Time 0.6

10-10-17	Permit 2016-03, 22 Colby Hill Road. Stopped by and he was home. Inspected the completed area above the garage. Looked okay and an egress window in the bedroom. Garage upstairs contained a bedroom, kitchen, bathroom, laundry area, and a lounge area. Walked through rest of house and it was okay. One thing I told him is that the door from the garage to the house should have a fire rated door as the walls and ceiling are fire rated sheetrock. I will issue the CO.

Time 0.3

David H Lersch                                                                 Plainfield Building Inspector